## Slide 1
Deep Learning

## Slide 2
Machine Learning: Regression
available dataset
parametric model
Loss (MSE)
Real estate application

## Slide 3
Basic units for Neural Networks
Σ
x1
x2
xd
w2
w1
wd
1
b
z
nonlinear activation function
We have a non-linear relation between inputs and outputs!

## Slide 4
Fully-connected Feedforward Neural Networks
Move from one neuron to a hierarchical structure with fully connected neurons
Input layer
Layer 2
Output layer
Layer 3
We can easily define a NARX structures parameterized by the weights (and biases) of the network

## Slide 5
FFN: PyTorch
Definition of the model class
Instantiate the model class, run and show model

## Slide 6
FFN: Training in PyTorch

## Slide 7
Exercise description: F-16 Ground Vibration Test
Nonlinear benchmarks: https://www.nonlinearbenchmark.org/benchmarks/f-16-gvt
Ground Vibration Test of an F-16 aircraft, a key process in assessing the structural integrity and dynamic behavior of the aircraft under various conditions
Dummy payloads mounted at the wing tips.
Goal: understand how the aircraft responds to vibrations
Instrumentation: shaker was attached beneath the right wing to generate input signals, and accelerometers used to measure vibrations
Nonlinearities due to mounting interfaces of the two payloads

## Slide 8
Exercise description: F-16 Ground Vibration Test
Inputs:
  voltage measured at the output of the signal generator amplifier, acting as a reference input,
  actual force provided by the shaker and measured by an impedance head at the excitation location.
Outputs: acceleration signals measured:
  at the excitation location,
  on the right wing next to the interface,
  on the payload next to the interface
Models:
  Three independent NARX models, one for each output (optional: unique model with 3 outputs)
  Regressor for the i-th model
Performance:
  Simulation in test data (also check one-step ahead prediction)
  Metrics: RMSE and/or R2 coefficient

## Slide 9
Recurrent Neural Networks (RNNs)
Architectures tailored to process time series data and temporal information (audio, text, video, signals, etc. )
u(t)
h(t)
u(t+T)
h(t+T)
unfold
u(t)
h(t)
u(t+1)
h(t+1)
u(t+2)
h(t+2)
…
h(t-1)
or skip some initial samples

## Slide 10
u(t)
u(t+1)
u(t+2)
…
…
…
Multi-layer RNN
…
…
…
…
Hidden states of a layer are also inputs of the next layer
u(t+2)
u(t+T)

## Slide 11
u(t)
u(t+1)
u(t+2)
…
…
…
Bidirectional RNN
…
…
…
…
Causality is lost. Might not be useful for prediction, but for tasks like smoothing
u(t+2)
u(t+T)

## Slide 12
Creating training data
Given an input/output sequence of length T, we can unfold the network up to T steps (you simulate T-step time ahead)
… or we can split the sequence into shorter sub-sequences (overlapped or not) of length L<<T, and thus create batch of sub-sequences. Network is unfolded for L steps (when you train, you predict L-step time ahead)

## Slide 13
Vanilla Recurrent Neural Network
u(t)
h(t)

## Slide 14
Recurrent Neural Networks: Pytorch

## Slide 15
LSTM: Long Short-Term Memory Neural Networks
u(t)
h(t)
Image by Guillaume Chevalier, CC BY-SA 4.0, via Wikimedia Commons
Hochreiter, S., & Schmidhuber, J. (1997). Long short-term memory. Neural Computation, 9(8), 1735–1780
h(t)
c(t)

## Slide 16
Backpropagation

## Slide 17
Back-propagation I
Layer 1
Layer 2
Layer 3
What we want:
Idea: Back propagate
Layer 1
Layer 2
Layer 3

## Slide 18
Back-propagation II
Focus on Layer L
Layer L
We have an interface to connect blocks/layers and recursively compute the derivatives!
Technicalities
Sigmoid activation function:
; (1- )
Linear layer:
Algorithm: reverse-mode automatic differentiation. Application to neural network training is called back-propagation.
Baydin, A. G., Pearlmutter, B. A., Radul, A. A., & Siskind, J. M. (2018). Automatic differentiation in machine learning: a survey. Journal of machine learning research, 18(153), 1-43.