## Slide 1: Meta Learning for System Identification
Marco Forgione
Dalle Molle Institute for Artificial Intelligence, USI-SUPSI, Lugano, Switzerland
Leuven, June 19, 2026

## Slide 2: Motivation
Machine learning models can effectively describe a wide variety of dynamical systems
However, training is computationally expensive and data-hungry
Can we automate the design of algorithms, model structures, optimizers for a class of system identification problems?
This is meta learning, aka learning to learn!

## Slide 3: The “sines” meta learning toy example
Regression datasets : sines with randomized phase and amplitude
Simple structure, but just points per dataset
Would be trivial with points per dataset, or if we the knew the true model structure
Example from:
Finn, Chelsea, Pieter Abbeel, and Sergey Levine. "Model-agnostic meta-learning for fast adaptation of deep networks.” International conference on machine learning. PMLR, 2017.

## Slide 4: The “sines” meta learning toy example
With a black-box structure (e.g., a small neural net) we overfit the data points
If we knew the structure, data points would be enough to find
What if we observe points from many datasets? Can we learn the pattern?
Results with existing meta learning approaches

## Slide 5: From standard to meta system identification
System Identification
  Dataset: I/O trajectory of one particular system
  Objective: estimate a model from
  is fixed (or manually tuned)
Meta System Identification
  Meta dataset: collection of datasets from similar systems
  Objective: learn to make prediction on all systems in
  is learned!
model-based meta learning
in-context learning

## Slide 6: From algorithm learning to in-context learning
in-context learning
algorithm learning
meta model
Meta dataset: collection of datasets from different yet similar systems
Objective: learn an algorithm
4

## Slide 7: In-context system identification
Particular dynamical system:
  Input/output context data, input query predicted query output:
meta-model
Forgione, M., Pura, F., & Piga, D. (2023). From system models to class models: An in-context learning paradigm. IEEE Control Systems Letters, 7, 3513-3518.

## Slide 8: Large Language Model analogy
Output (Claude Sonnet 4.6)
Grote Markt & Town Hall — the obvious starting point. The 15th-century Gothic Town Hall is one of the most extravagantly decorated secular buildings in all of Belgium: every surface bristles with carved statues and tracery.
Saint Peter's Church — don't just glance at the exterior. Inside you'll find major works by Dierick Bouts, the 15th-century Flemish master who spent most of his career in Leuven. His Last Supper altarpiece is here. There's also a small crypt worth descending into.
Context
A user is passionate about history and is planning a trip to Leuven.
Query
Can you recommend some places to visit?

## Slide 9: Meta model architecture
Meta-model extended to process the query’s input/output initial condition
Parameterized as a Transformer
Rufolo, M., Piga, D., Maroni, G., & Forgione, M. (2025). Enhanced Transformer architecture for in-context learning of dynamical systems. ECC 2025.

## Slide 10: Meta model training
STEPS
Collect a meta dataset of similar systems from a simulator:
Meta training offline to estimate a meta-model :
Make predictions on new (real) system, in a zero-shot fashion (no training):
, i=1,2,…,∞
Technically, it is just a supervised learning problem – standard training.
The trained may be seen as a learned identification + simulation algorithm…
… or as a specialized question answering system – a kind of SYSID GPT.

## Slide 11: Meta Training – System class
Wiener-Hammerstein Systems
Sequential LTI LTI
Random LTI, order
: random feed-forward NN
Meta training on ~100 M simulated Wiener-Hammerstein systems
The input is a multisine signal with random phase and spectrum
White noise added to the simulated output
Transformer model with ~5 M parameters, training time ~1 day on an Nvidia 4090 GPU…

## Slide 12: Testing – Nonlinear benchmarks (www.nonlinearbenchmark.org)
Real Wiener-Hammerstein benchmark
RMSE * 1000 | Inference time (s)
1.4 | 5.91
State-of-the-art
Rufolo, M., Piga, D., Pura, F., & Forgione, M. (2025). In-Context Learning for System Identification: Recent Advances. Submitted to a journal, available here.

## Slide 13: Testing – Nonlinear benchmarks
Coupled Electric Drives (CED)
RMSE | Inference time (s)
[0.068,0.055] | 0.17
State-of-the-art
Rufolo, M., Piga, D., Pura, F., & Forgione, M. (2025). In-Context Learning for System Identification: Recent Advances. Submitted to a journal, available here.

## Slide 14: Testing – Nonlinear benchmarks
Cascaded tanks with Overflow
RMSE | Inference time (s)
0.429 | 0.22
State-of-the-art
Rufolo, M., Piga, D., Pura, F., & Forgione, M. (2025). In-Context Learning for System Identification: Recent Advances. Submitted to a journal, available here.

## Slide 15: Other objectives: meta state estimation
A meta state estimator that generalizes to different systems from the context
Experiments on speed estimation of BLDC motors
Colombo, A., Busetto, R., Breschi, V., Forgione, M., Piga, D., & Formentin, S. (2025). In-Context Learning for Zero-Shot Speed Estimation of BLDC motors. To be presented at IFAC World Congress 2026.
Busetto, R., Breschi, V., Forgione, M., Piga, D., & Formentin, S. (2024). In-context learning of state estimators. Presented at SYSID 2024.

## Slide 16: Whitening the meta-learning box
The meta-learning grayscale
  model-based meta learning in-context learning
In-context learning: prediction is a black-box function of dataset and new data.
Other extreme: learn hyper-parameters of algorithm that returns (interpretable) model parameters
  Learn the learning rate, initial value for gradient-based optimization (MAML), etc
Hospedales, T., Antoniou, A., Micaelli, P., & Storkey, A. (2021). Meta-learning in neural networks: A survey. IEEE transactions on pattern analysis and machine intelligence, 44(9), 5149-5169.

## Slide 17: Meta state estimation: whitening the box
Transformer returns estimator gain + physical parameters instead of predictions directly.
On-going work with Université de Poitiers (Hugo Koide, Guillaume Mercère)
  Model-based meta learning
In-context learning

## Slide 18: Conclusions
Takeaways:
In-context system identification, estimation, & control
Off-line: learn how to map data into prediction
On-line: provide context data, query input query output (zero shot)
Current activities:
Real-world applications
Whitening the meta-learning box
Providing guarantees
Algorithm discovery with LLM-driven agents

## Slide 19
Recent topics in system identification: learning models for decision and control
- Special Issue from IFAC SYSID 2027
Submission deadline: 01 October 2026
This special issue highlights leading papers from the IFAC SYSID 2027 Symposium
Executive guest editor: Dario Piga
Submission site already open
More info: https://conferences.ifac-control.org/sysid2027/
… or just ask us!

## Slide 20: Optimizing over unbounded domains with LLM-based coding agents
Meta learning as an optimization over parametrized algorithms: Find such that:
Algorithm search limited to a pre-defined space.
Can LLM-based agents suggest models & algorithms?
  Unbounded search space – LLMs can write code
  Objective can be in natural language
  Goes in the direction of automated research
19
D. Piga and M. Forgione. ASIA: an Autonomous System Identification Agent. arXiv, 2026.